## Slide 1: IceCube: Evolving Work Flows
Steve Barnet
University of Wisconsin – Madison
WIPAC

## Slide 2: Overview
The Basics of IceCube
Data Handling
Computing Model
Summary

## Slide 3: The IceCube Neutrino Observatory
A kilometer scale neutrino detector
Located at geographic South Pole
Detects Cherenkov light from neutrino interactions

## Slide 5: Location, Location, Location
Why the South Pole?
Lots of ice – a great detection medium
The ice is very clear
Thick ice sheet – sensors deep enough to provide significant background reduction

## Slide 6: IceCube Overview
400 people
39 Institutions
11 Countries
Exotic Locales

## Slide 9: Data Volume
Event rate of 3000 Hz
1 TB/day raw data
Reduced to 100 GB/day
  Based on available satellite bandwidth
Tapes shipped North every year

## Slide 10: Computing Model
University of Wisconsin - Madison – Tier 0
  Raw data collection and archive
  Data production to Level 3
  Coordinate simulation production
DESY-Zeuthen – Tier 1
  Second copy of Level 2 data
  Hold simulation data sets in Europe

## Slide 11: Tier 0 Capacity
Compute cluster
  1400 cores, memory at least 4 GB/core
  HTCondor managed
Experimental data
  1 PB Lustre filesystem
Simulation data
  1.2 PB Lustre filesystem
Analysis data sets
  250 TB Lustre filesystem

## Slide 12: Data Production
Level 1
  Filtered stream from Pole
Level 2 – Science Ready
  Calibrations, basic reconstructions
  Common processing needed by all analyses
Level 3 – set by each working group
  Event selection
  Stream separation

## Slide 13: Simulation Production
Driver of our distributed computing
Collaboration institutions contribute to simulation production
Production is coordinated with a central DB at UW Madison
Output is collected at either DESY-Zeuthen or UW Madison

## Slide 14: Simulation Framework
Software framework to coordinate components
Central DB at UW-Madison to coordinate and track production
First versions were monolithic – photonics tables made grids difficult
Newer versions broken into finer steps

## Slide 15: Simulation
Event generation
  CORSIKA for cosmic ray background
  Several neutrino generators
Photon propagation
  Lookup tables
  Direct simulation on GPUs
Detector simulation

## Slide 16: First Monolithic WorkFlow
This was a single job
A data set is O(100,000) jobs
Long Photonics chain
Lots of waiting
Multiple detectors simulated
Worked Locally, grids difficult

## Slide 17: OSG – Attempt 1
Refactor work flow using DAGMan
glideinWMS is now on the scene
+ lots of local caching and clever job routing

## Slide 18: Workable with caching

## Slide 19: Enter GZK-9000

## Slide 20: The Name
Or: what happens when you give clever grad students a mission and some time
Derived from HAL-9000 (2001: A Space Odyssey)
  IBM << 1 == HAL
  HAL << 1 == GZK
GZK is a predicted limit on the energy of cosmic rays

## Slide 21: The Hardware
6x Dell C6145 series chassis for CPUs
3x Dell C410 Chassis for GPUs
  16x GPUs each
  nVidia Tesla M2070

## Slide 22: The Place
CHTC pool
Shared resource – Available to other CHTC users
WID/MIR data center
29 U of rack space
15 KW power dissipation

## Slide 23: The Reason
Improves the science
  Eliminates many binning artifacts associated with tables
  Required many improvements to our understanding of the ice
Greatly reduces the need for Photonics tables

## Slide 24: Simplifies the Work Flow

## Slide 25: OSG Attempt 2
Move top tier of DAG to OSG
Results:
  GPU processing at UW
  Use local GPUs if available
Turns our “tables problem” into a data movement problem – may be more tractable

## Slide 26: Approach
Start small scale with CHTC resources
  Submit machine and glideinWMS
  Shake out the bugs and surprises
Add IceCube resources as needed to feed the beast
  CVMFS – software distribution, remaining tables
  Squid caching
  Expand gridFTP service

## Slide 27: Future Workloads
Analysis – get Jane the Physicist doing regular analysis using OSG
Data processing (Level 2 production)
Reformatting old data into archival format

## Slide 28: GPUs
Better integration with HTCondor
CPU/GPU ratios – 2:1, 1:4 - ?
Limit jobs to assigned GPUs

## Slide 29: Summary
IceCube is a km scale neutrino detector
Work well locally with HTCondor
Expanding to OSG – involves work
Extensive use of GPUs
We may not be the coolest experiment on the planet, but we are one of the coldest.

## Slide 30: Credits
Juan Carlos Diaz-Velez, David Schultz – IceProd framework
Dima Chirkin, Claudio Kopper – GPU simulation development
Heath Skarlupka – GPU wrangling
CHTC – Hosting the GZK cluster, OSG support, HTCondor GPU efforts
UW Madison – Fast networks
NSF – IceCube M&O funding

## Slide 31: Questions?