## Slide 1: Crossing Guard: Mediating Host-Accelerator Coherence Interactions
Lena E. Olson*, Mark D. Hill, David A. Wood
University of Wisconsin-Madison * Now at Google
ASPLOS 2017 April 10th, 2017

## Slide 2: Accelerators are here!
Complex, programmable accelerators increasingly prevalent
Many applications: graphics, scientific computing, video encoding, machine learning, etc…
Accelerators may benefit from cache coherent shared memory
May be designed by third parties

## Slide 3: However…
Host coherence protocols may be proprietary and complex
Bugs in accelerator implementations might crash host system!
Crossing Guard: coherence interface to safely translate accelerator ↔ host protocol
Accel $
XG
Host $
Hello!
你好!
Accel
CPU

## Slide 4: Outline
Goals
Design
Guarantees
Evaluation

## Slide 5: Crossing Guard Goals
When adding accelerators to host coherence protocol:
Allow accelerators customized caches
Simple, standardized accelerator coherence interface
Guarantee safety for the host system

## Slide 6: 1. Why Customize Caches?
CPU caches have to work with most types of workloads
Accelerators may only run some workloads!
  Optimize caches for likely data access patterns
  Number of levels, writeback vs. writethrough, MSI vs VI, etc.
Accel
Accel
Accel
Accel
Accel
L1 $
L1 $
L2 $
L1 $
L1 $
VI
L1 $
Accel
VI
L1 $
L2 $

## Slide 7: 2. Why Simple, Standardized Interface?
Host systems speak different protocols…
Expensive to redesign for each one!
  Intel, AMD, ARM, IBM, Oracle…
  CCIX shows industry cares!
Accel
L1 $
Host Directory
Hello?
你好?
Hej?
Bonjour?

## Slide 8: 2. Why Simple, Standardized Interface?
(Transition table in style of Sorin et al.)
L1 controller from gem5’s MOESI_hammer
Events
States

## Slide 9: 3. Why Host Safety?
Addr State
A S
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
Addr State
A I
Directory
Accel Cache (#0)
Cache #1
Cache #2
Accel
CPU
CPU

## Slide 10: 3. Why Host Safety?
Addr State
A S
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
Ack
Addr State
A I
Directory
Accel Cache (#0)
Cache #1
Cache #2
? ? ?
? ? ?

## Slide 11: 3. Why Host Safety?
Addr State
A I
Addr State Owner/Sharers Req
A MT 0 -
Addr State
A M
Addr State
A I
Directory
Accel Cache (#0)
Cache #1
Cache #2
Inv
Req: dir
Addr State Owner/Sharers Req
A MT_I 0 -

## Slide 12: Outline
Goals
Design
Guarantees
Evaluation

## Slide 13: Crossing Guard
Hardware translating between host and accelerator protocols
Set of accelerator ↔ host coherence messages (like an API)
Accel $
XG
Host $
Hello!
你好!
Accel
CPU

## Slide 14: Crossing Guard Interface
Accelerator  Host Requests
GetS, GetM
PutS, PutE, PutM
Host  Accelerator Responses
DataS, DataE, DataM
Writeback Ack
Host  Accelerator Requests
Invalidate
Accelerator  Host Responses
InvAck, Clean Writeback,
Dirty Writeback

## Slide 15: Crossing Guard
Hides implementation details of host protocol
  No counting acks, sending unblocks, handling races, etc.
Moves protocol complexity into Crossing Guard hardware
  Only implemented once per host system
  By experts!

## Slide 16: Experimental Implementation
Coherence controllers / protocols implemented in slicc
Simulations using gem5
Code and transition tables available online
http://research.cs.wisc.edu/multifacet/xguard/

## Slide 17: Outline
Goals
Design
Guarantees
Evaluation

## Slide 18: 1. Customize Caches
Designed + implemented two sample systems
Accel L1
Accel L1
Accel L1
CPU L1
CPU L1
Host Directory / L2
XG
XG
XG
Private Per-Core L1 at Accelerator

## Slide 19: 1. Customize Caches
Designed + implemented two sample systems
Accel L1
Accel L1
Accel L1
CPU L1
CPU L1
Host Directory / L2
XG
Private L1s + Shared L2 at Accelerator
Accel L2

## Slide 20: 2. Simple, Standardized Interface
Controller | States | Transitions
AMD Hammer-like Private $$ | 24 | 148
Crossing Guard Single-Level Private L1 | 5 | 20
Single-level Accelerator Cache using Crossing Guard Interface

## Slide 21: 2. Simple, Standardized Interface
Implemented Crossing Guard controller for two host protocols
  AMD Hammer-like Exclusive MOESI
  Two-Level MESI Inclusive
Modularity: Host and Accelerator protocol choice is completely independent

## Slide 22: 2. Simple, Standardized Interface
Addr State Acks Reqs Timer
A I 0 - 0
Addr State Acks Reqs Timer
A IM 0 - 0
Addr State Acks Reqs Timer
A SM -2 - 0
Addr State Acks Reqs Timer
A SM -1 - 0
Addr State Acks Reqs Timer
A M 0 - 0
Addr State
A I
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
Addr State
A S
Addr State
A B
GetM
GetM
Addr State Owner/Sharers Req
A SM_MB 1, 2 0
Inv
Req: 0
Ack
Data
Acks:-2
Addr State
A I
Ack
DataM
Addr State
A M
Directory
Accel Cache
Cache #1
Cache #2
Cache #0
UnblockM
Addr State Owner/Sharers Req
A M 0 -

## Slide 23: 2. Simple, Standardized Interface
Addr State Acks Reqs Timer
A I 0 - 0
Addr State Acks Reqs Timer
A IM 0 - 0
Addr State Acks Reqs Timer
A SM -2 - 0
Addr State Acks Reqs Timer
A SM -1 - 0
Addr State Acks Reqs Timer
A M 0 - 0
Addr State
A I
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
Addr State
A S
Addr State
A IM
GetM
GetM
Addr State Owner/Sharers Req
A SM_MB 1, 2 0
Ack
Data
Acks:-2
Addr State
A I
Ack
DataM
Addr State
A M
Directory
Accel Cache
Cache #1
Cache #2
Cache #0
UnblockM
Addr State Owner/Sharers Req
A M 0 -

## Slide 24: 3. Host Safety
Addr State Acks Reqs Timer
A I 0 - 0
Addr State
A S
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
Ack
Addr State
A I
Directory
Accel Cache
Cache #1
Cache #2
Cache #0

## Slide 25: 3. Host Safety
Addr State Acks Reqs Timer
A M 0 - 0
Addr State
A S
Addr State Owner/Sharers Req
A MT 0 -
Addr State
A M
Addr State
A I
Directory
Accel Cache
Cache #1
Cache #2
Cache #0
Inv
(Req: dir)
Addr State Owner/Sharers Req
A MT_I 0 -
Addr State Acks Reqs Timer
A MI 0 dir 1210
Inv
Time:
200
Time:
210
Time:
500
Time:
1000
Time:
1500
Data
Addr State Acks Reqs Timer
A I 0 - 1210
Addr State Owner/Sharers Req
A WB 0 -

## Slide 26: Outline
Goals
Design
Guarantees
Evaluation

## Slide 27: Evaluation
Does it provide coherence to correct accelerator?
Does it provide safety to host?
Does it allow high performance?

## Slide 28: I. Correctness Testing
Are coherence invariants are maintained when accelerator is acting correctly?
How? Random tester
  Store-Load pairs to random addresses
  Check integrity of data
Ran for 160 billion load/store pairs
Local coverage: 100% states, 100% events, > 99% transitions

## Slide 29: II. Fuzz Testing
Is host safety maintained when accelerator misbehaves?
How? Replace accelerator cache with evil controller
  Generates random coherence messages to random addresses
  Desired outcome: No deadlocks / crashes
Ran for 7 billion load/store pairs
Local Coverage: 100% states, 100% events, > 99% transitions

## Slide 30: III. Performance Testing
gem5-gpu
Rodinia workloads
MESI Inclusive host protocol
Normalized Accelerator Execution Time
Benchmark

## Slide 31: Crossing Guard Summary
Provides simple, standardized interface to ease accelerator development
Correctness when accelerator is correct
Host safety when accelerator is incorrect
Low performance overhead

## Slide 32: Questions?
? ? ?
? ? ?

## Slide 33: Backup Follows

## Slide 34: Two-Level Accelerator Protocol (1)
Accel L1
Accel L1
Accel L1
CPU L1
CPU L1
Host Directory / L2
XG
Private L1s + Shared L2 at Accelerator
Accel L2

## Slide 35: Two-Level Accelerator Protocol (2)
L1 Controller (M state contains dirty/clean bit)

## Slide 36: Two-Level Accelerator Protocol (3)
L2 Controller
(Coordinates Sharing among Accelerator L1s)

## Slide 37: Crossing Guard Invariants
Crossing Guard Guarantees to Host:
Accelerator requests must be correct
  Consistent with block stable state at accelerator
  Consistent with block transient state at accelerator
Accelerator responses must be correct
  Consistent with block stable state at accelerator
  Consistent with block transient state at accelerator
  Received within a reasonable time
( + Border Control Protections!)

## Slide 38: Crossing Guard Variants
Full State Crossing Guard
  Inclusive directory of accelerator state
  + Places few restrictions on host protocol
  + Can hide all errors
  - Requires tag + metadata storage for all blocks
Transactional Crossing Guard
  Stores only data for in-flight transactions
  + Small storage
  + Provides most safety properties
  - Requires some host tolerance

## Slide 39: Single-Level Cache

## Slide 40: Simulation Parameters

## Slide 41: Time Spent Simulating (Random)
Configuration | Time
XG Full + Hammer + 1 Level | 5.28 years
XG Full + Hamer + 2 Level | 2.51 years
XG Full + MESI Inc + 1 Level | 133 days
XG Full + MESI Inc + 2 Level | 223 days
XG Trans. + Hammer + 1 Level | 3.17 years
XG Trans. + Hammer + 2 Level | 1.38 years
XG Trans + Inc + 1 Level | 90 days
XG Trans + Inc + 2 Level | 103 days
TOTAL | 13.9 years

## Slide 42: Full Coverage %s (Random)
Full State XG | Single-level | Two-level
Hammer-like | 99 | 99.8
MESI Inclusive | 100 | 99.4
Transactional XG | Single-level | Two-level
Hammer-like | 99.3 | 99.5
MESI Inclusive | 100 | 99.7

## Slide 43: Time Spent Simulating (Fuzz)
Configuration | Time
XG Full + Hammer-like | 1.62 years
XG Full + MESI Inclusive | 287 days
XG Transactional + Hammer-like | 5.3 years
XG Transactional + MESI Inclusive | 41 days
Total | 7.82 years

## Slide 44: Full Coverage %s (Fuzz)
Full State Crossing Guard | Fuzz Tester
Hammer-like | 99.3
MESI Inclusive | 99.7
Transactional Crossing Guard | Fuzz Tester
Hammer-like | 99.7
MESI Inclusive | 100

## Slide 45: PutS Accelerator Messages
Why?
  Some host protocols use them
  Simplify management of Full State Crossing Guard
  Cannot implement Transactional Crossing Guard + host protocol with PutS without them
Bandwidth Impact
  Carry no data
  Only between accelerator cache  Crossing Guard, not host system
  ~1-4% of that bandwidth in experiments.
  Could be reduced by setting a flag at Crossing Guard.

## Slide 46: Why not Model Checking?
Model checking is useful! Industrial implementation of Crossing Guard would use.
Academic tools have limitations 
  Benefit from symmetry, but Crossing Guard system asymmetric
  May only work with one block in system
  Substantial implementation overhead
This work was a proof of concept
  Random / Fuzz testing not perfect, but results suggestive.
  Even models can have mistakes!

## Slide 47: Performance: Hammer-like

## Slide 48: Performance: MESI Inclusive

## Slide 49: Performance (Hammer-like)

## Slide 50: Template
Addr State Acks Reqs Timer
A I 0 - 0
Addr State
A I
Addr State Owner/Sharers Req
A SS 1, 2 -
Addr State
A I
GetM
GetM
Addr State
A I
Ack
Directory
Accel Cache
Cache #1
Cache #2
Cache #0

## Slide 51: Old Slides

## Slide 52: 3. Why Host Safety?
Accelerator cache
Directory
Addr A: ?
Addr A: RW
Addr A: Not Present in caches
? ? ?
? ? ?
Ack
Addr: A

## Slide 53: 3. Why Host Safety?
Directory
Accelerator cache
Addr A: M
Addr A: RW
Addr A: M, owned by accelerator
Fwd-GetM
Addr: A

## Slide 54: Crossing Guard Example
Directory
Accelerator cache
Addr A: M
Addr A: RW
Addr A: M, owned by accelerator
A: waiting for WB
Writeback
Addr: A
Fwd-GetM
Addr: A
Invalidate
Addr: A

## Slide 55: Crossing Guard Example
Directory
Accelerator cache
Addr A: M
Addr A: RW
Addr A: M, owned by accelerator
A: waiting for WB
Invalidate
Addr: A
Writeback
Addr: A
Fwd-GetM
Addr: A