## Slide 1: Redundant Memory Mappings for Fast Access to Large Memories
Vasileios Karakostas, Jayneel Gandhi, Furkan Ayar,
Adrián Cristal, Mark D. Hill, Kathryn S. Mckinley, Mario Nemirovsky, Michael M. Swift, Osman S. Ünsal
Notes: Provide Title and introduce everyone.

## Slide 2: Executive Summary
Problem: Virtual memory overheads are high (up to 41%)
Proposal: Redundant Memory Mappings
  Propose compact representation called range translation
  Range Translation – arbitrarily large contiguous mapping
  Effectively cache, manage and facilitate range translations
  Retain flexibility of 4KB paging
Result:
  Reduces overheads of virtual memory to less than 1%

## Slide 3: Outline
Motivation 
  Virtual Memory Refresher + Key Technology Trends
  Previous Approaches
  Goals + Key Observation
Design: Redundant Memory Mappings
Results
Conclusion

## Slide 4: Virtual Memory Refresher
TLB
(Translation Lookaside Buffer)
Process 1
Process 2
Virtual Address Space
Physical Memory
Page Table
Challenge: How to reduce costly page walks?

## Slide 5: Two Technology Trends
*Inflation-adjusted 2011 USD, from: jcmit.com
Chart: Memory capacity for $10,000*
  TLB reach is limited
Year | Processor | L1 DTLB entries
1999 | Pent. III | 72
2001 | Pent. 4 | 64
2008 | Nehalem | 96
2012 | IvyBridge | 100
2015 | Broadwell | 100

## Slide 6: 0. Page-based Translation
Virtual Memory
VPN0 PFN0
TLB
Physical Memory
Notes: Benefits
+ Most flexible
+ Only 4KB alignment required
Disadvantage
─ Requires more TLB entries
─ Limited TLB reach

## Slide 7: 1. Multipage Mapping
Virtual Memory
Clustered TLB
[ASPLOS’94, MICRO’12 and HPCA’14]
Physical Memory
Sub-blocked TLB/CoLT
VPN(0-3) PFN(0-3)
Bitmap
Map
Notes: Benefits
+ Increased the TLB reach by 8X-32X
+ Clustering of pages allowed
Disadvantages
─ Requires size alignment
─ Contiguity required

## Slide 8: 2. Large Pages
Virtual Memory
Physical Memory
[Transparent Huge Pages and libhugetlbfs]
VPN0 PFN0
Large Page TLB
Notes: Benefits
+ Increases TLB reach
+ 2MB and 1GB page size in x86-64
Disadvantages
─ Size alignment restriction
─ Contiguity required

## Slide 9: 3. Direct Segments
Virtual Memory
Direct Segment
(BASE,LIMIT)  OFFSET
BASE
LIMIT
OFFSET
[ISCA’13 and MICRO’14]
Physical Memory
Notes: Benefits
+ Unlimited reach
+ No size alignment required
Disadvantages
─ One direct segment per program
─ Not transparent to application
─ Applicable to big-memory workloads

## Slide 10: Can we get best of many worlds?
 | Multipage Mapping | Large Pages | Direct Segments | Our Proposal
Flexible alignment |  |  |  | 
Arbitrary reach |  |  |  | 
Multiple entries |  |  |  | 
Transparent to applications |  |  |  | 
Applicable to all workloads |  |  |  | 

## Slide 11: Key Observation
Virtual Memory
Physical Memory

## Slide 12: Key Observation
Virtual Memory
Large contiguous regions of virtual memory
Limited in number: only a few handful
Physical Memory
Code
Heap
Stack
Shared Lib.

## Slide 13: Compact Representation: Range Translation
Virtual Memory
Physical Memory
BASE1
LIMIT1
OFFSET1
Range Translation 1
Range Translation: is a mapping between contiguous virtual pages mapped to contiguous physical pages with uniform protection

## Slide 14: Redundant Memory Mappings
Virtual Memory
Physical Memory
Range Translation 1
Range Translation 2
Range Translation 3
Range Translation 4
Range Translation 5
Map most of process’s virtual address space redundantly with modest number of range translations in addition to page mappings

## Slide 15: Outline
Motivation
Design: Redundant Memory Mappings 
  A. Caching Range Translations
  B. Managing Range Translations
  C. Facilitating Range Translations
Results
Conclusion

## Slide 16: A. Caching Range Translations
V47 …………. V12
P47 …………. P12
L1 DTLB
L2 DTLB
Range TLB
Page Table Walker
Enhanced Page Table Walker

## Slide 17: A. Caching Range Translations
Hit
V47 …………. V12
P47 …………. P12
L1 DTLB
Range TLB
Enhanced Page Table Walker
L2 DTLB

## Slide 18: A. Caching Range Translations
Miss
V47 …………. V12
P47 …………. P12
L1 DTLB
Range TLB
Enhanced Page Table Walker
L2 DTLB
Hit
Refill

## Slide 19: A. Caching Range Translations
Miss
V47 …………. V12
P47 …………. P12
L1 DTLB
Range TLB
Enhanced Page Table Walker
L2 DTLB
Hit
Refill

## Slide 20: A. Caching Range Translations
Miss
V47 …………. V12
P47 …………. P12
L1 DTLB
Range TLB
L2 DTLB
Hit
Refill
Entry 1
BASE 1
LIMIT 1
≤
>
Entry N
BASE N
LIMIT N
≤
>
OFFSET 1 Protection 1
OFFSET N Protection N
L1 TLB Entry Generator Logic:
(Virtual Address + OFFSET) Protection

## Slide 21: A. Caching Range Translations
Miss
V47 …………. V12
P47 …………. P12
L1 DTLB
Range TLB
Enhanced Page Table Walker
L2 DTLB
Miss
Miss

## Slide 22: B. Managing Range Translations
Stores all the range translations in a OS managed structure
Per-process like page-table
Range Table
CR-RT
RTC
RTD
RTF
RTG
RTA
RTB
RTE

## Slide 23: B. Managing Range Translations
A) Page Table
B) Range Table
C) Both A) and B)
D) Either?
On a L2+Range TLB miss, what structure to walk?
Is a virtual page part of range? – Not known at a miss

## Slide 24: B. Managing Range Translations
Redundancy to the rescue
One bit in page table entry denotes that page is part of a range
Page Table Walk
1
Insert into L1 TLB
2
Application resumes memory access
3
Range Table Walk (Background)
Insert into Range TLB
Part of a range
CR-RT
RTC
RTD
RTF
RTG
RTA
RTB
RTE
CR-3

## Slide 25: C. Facilitating Range Translations
Virtual Memory
Physical Memory
Does not facilitate physical page contiguity for range creation
Demand Paging

## Slide 26: C. Facilitating Range Translations
Virtual Memory
Physical Memory
Allocate physical pages when virtual memory is allocated
Increases range sizes  Reduces number of ranges
Eager Paging

## Slide 27: Outline
Motivation
Design: Redundant Memory Mappings
Results 
  Methodology
  Performance Results
  Virtual Contiguity
Conclusion

## Slide 28: Methodology
Measure cost on page walks on real hardware
  Intel 12-core Sandy-bridge with 96GB memory
  64-entry L1 TLB + 512-entry L2 TLB 4-way associative for 4KB pages
  32-entry L1 TLB 4-way associative for 2MB pages
Prototype Eager Paging and Emulator in Linux v3.15.5
  BadgerTrap for online analysis of TLB misses and emulate Range TLB
Linear model to predict performance
Workloads
  Big-memory workloads, SPEC 2006, BioBench, PARSEC

## Slide 29: Comparisons
4KB: Baseline using 4KB paging
THP: Transparent Huge Pages using 2MB paging [Transparent Huge Pages]
CTLB: Clustered TLB with cluster of 8 4KB entries [HPCA’14]
DS: Direct Segments [ISCA’13 and MICRO’14]
RMM: Our proposal: Redundant Memory Mappings [ISCA’15]

## Slide 30: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
Measured using performance counters
Modeled based on emulator
5/14 workloads
Rest in paper
Assumptions:
CTLB: 512 entry fully-associative
RMM: 32 entry fully-associative
Both in parallel with L2
Notes: Make this animated and add points to raise.

## Slide 31: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
Overheads of using 4KB pages are very high
Notes: Make this animated and add points to raise.

## Slide 32: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
Clustered TLB works well, but limited by 8x reach
Notes: Make this animated and add points to raise.

## Slide 33: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
2MB page helps with 512x reach: Overheads not very low
Notes: Make this animated and add points to raise.

## Slide 34: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
Direct Segment perfect for some but not all workloads
Notes: Make this animated and add points to raise.

## Slide 35: Performance Results
Chart: Execution Time Overhead
| 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | 4KB | CTLB | THP | DS | RMM | cactusADM | canneal | graph500 | mcf | tigr
Measured | 0.38951 | 0.13476 | 0.1313 | 0.058699 | 0.29232 | 0.061808 | 0.41617 | 0.17367 | 0.35541 | 0.10242
Modeled | 0.1807 | 8.6237e-07 | 0.002453 | 0.1044 | 0.076417 | 0.0039529 | 0.29068 | 2.9232e-05 | 0.0014082 | 0.4003 | 0.00055478 | 0.0025899 | 0.34908 | 0.17328 | 0.01063
RMM achieves low overheads robustly across all workloads
Notes: Make this animated and add points to raise.

## Slide 36: Why low overheads? Virtual Contiguity
Benchmark | Paging | Ideal RMM ranges | 
 | 4KB + 2MB THP | # of ranges | #of ranges to cover more than 99% of memory
cactusADM | 1365 + 333 | 112 | 49
canneal | 10016 + 359 | 77 | 4
graph500 | 8983 + 35725 | 86 | 3
mcf | 1737 + 839 | 55 | 1
tigr | 28299 + 235 | 16 | 3
1000s of TLB entries required
Only 10s-100s of ranges per application
Only few ranges for 99% coverage

## Slide 37: Summary
Problem: Virtual memory overheads are high
Proposal: Redundant Memory Mappings
  Propose compact representation called range translation
  Range Translation – arbitrarily large contiguous mapping
  Effectively cache, manage and facilitate range translations
  Retain flexibility of 4KB paging
Result:
  Reduces overheads of virtual memory to less than 1%

## Slide 38: Questions ?