## Slide 1: Hands-Off Persistence System (HOPS)
Swapnil Haria1, Sanketh Nalli1, Haris Volos2,
Kim Keeton2, Mark D. Hill1, Mike M. Swift1
1 University of Wisconsin-Madison
2 Hewlett Packard Labs
Notes: Hey Everyone, today I will be describing our new hardware design for simplifying the programming of PM system.

## Slide 2: WHISPER Analysis HOPS Design
4% accesses to PM, 96% to DRAM
5-50 epochs/transaction
Self-dependencies common
Cross-dependencies rare
Volatile memory hierarchy (almost) unchanged
Order epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method based on coherence
Notes: Analysis preceeds good design. Our analysis of PM applications from the WHISPER suite, which I will recap now, guides our design of the HOPS.
We observed that a majority of accesses are to DRAM. Thus, any HW support for PM should not hurt the performance of volatile accesses. For example, this precludes adding state to the caches which would increase the access latency of all accesses. Thus, HOPS leaves the volatile memory structures untouched.
We noticed that transactions can comprise as many as 50 epochs, resulting in frequent flushing and low performance. But these greatly simply the programming of PM systems. So HOPS provides a mechanism for ordering epochs without flushing.
We found that self-dependencies are common for epochs updating logs and metadata. Thus to avoid flushing, HOPS allows multiple copies of the same cacheline to co-exist.
Finally we saw that cross-thread dependencies are quite rare. For correctness, HOPS uses a conservative method based on coherence to track these dependencies.

## Slide 3: Outline
Motivation
HOPS Design
Evaluation
PM
HEAD
C
A
B
Chart: Normalized Speedup
| ctree | hashmap | echo | nstore | vacation | average
CLWB+Fence | 1 | 1 | 1 | 1 | 1 | 1
HOPS | 1.17 | 1.33 | 1.06 | 1.3 | 1.21 | 1.2
No-Flush | 1.67 | 1.59 | 1.18 | 1.49 | 1.25 | 1.41
?

## Slide 4: ACID Transactions (currently)
Acquire Lock
Release Lock
Prepare Log Entry
1
N
Mutate Data Structure
1
N
Commit Transaction
FLUSH EPOCH
FLUSH EPOCH
FLUSH EPOCH
Notes: While PM promises the best of both worlds - Disk and DRAM, it is quite tricky to program these systems. For crash-consistent and recoverable applications, programmers are forced to worry about flushing cachelines in the right order, and fencing properly. Thankfully, Libraries like Mnemosyne and NVML help by supporting ACID transactions, which simplify programming tremendously.

## Slide 5: Base System
Shared LLC
DRAM Controller
PM Controller
Persistent
Private L1
Private L1
Volatile
CPU 0
CPU 1
Notes: To understand why flushes are expensive, let's consider our system first. The address space would be partitioned into volatile and persistent regions. Each of these regions will be managed by one or multiple memory controllers. The cores will interact with these via the coherent cache hierarchy.

## Slide 6: Base System: Flush
1. Flush A
DRAM Controller
PM Controller
Persistent
Volatile
A=1
1. Flush A
Writeback A
Long Latency PM Write
Flush ACK
2. Flush B
CPU 0
CPU 1
Notes: When a CPU issues a flush request, the dirty cacheline is written back from one level of the hierarchy to the next, all the way to the PM controller. There is a long-latency PM write, after which the ACK has to propagate back before the core can proceed. Flushes can be overlapped, but only within an epoch, so it doesn’t help much.

## Slide 7: Outline
Motivation
HOPS Design
Evaluation
PM
HEAD
C
A
B
Chart: Normalized Speedup
| ctree | hashmap | echo | nstore | vacation | average
CLWB+Fence | 1 | 1 | 1 | 1 | 1 | 1
HOPS | 1.17 | 1.33 | 1.06 | 1.3 | 1.21 | 1.2
No-Flush | 1.67 | 1.59 | 1.18 | 1.49 | 1.25 | 1.41
?

## Slide 8: Hands-off Persistence System (HOPS)
Volatile memory hierarchy (almost) unchanged
Order epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method for handling cross-dependencies
Notes: Let’s take a look at our proposal now.
To avoid touching volatile memory, we add a new path for persistent writes to propagate to PM.

## Slide 9
+
Stores
CPU
Shared LLC
CPU
DRAM Controller
PM Controller
Persistent
Private L1
Private L1
Volatile
Persist Buffer
Front End
Persist Buffer
Front End
Persist Buffer
Back End
Loads + Stores
Loads
Base System + Persist Buffers
Base System
Notes: Unlike non-temporal writes, this new path is redundant to the caches and enforces ordering. These Persist Buffers are responsible for propagating PM writes to the PM in order. PM stores also update the volatile caches, but this is only to serve data reuse. Caches do not write back to PM.

## Slide 10
Volatile buffers
Front End (per-thread)
  Address, Ordering Info
Back End (per-MC)
  Cacheline data
Enqueue/Dequeue only
  Not fully-associative
Persist Buffers
Notes: Looking more closely at our PBs, they are volatile. They are split into the Front End, which is a small per-thread structure located at the L1 caches, which contain the address and some ordering infomation. The Back-End is much larger and is stored with the MCs, and stores the cacheline data for each entry. The Persist Buffers only needs to support enqueue and dequeue operations, and so they are not fully-associative structures.

## Slide 11: Hands-off Persistence System (HOPS)
Volatile memory hierarchy (almost) unchanged
Order epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method for handling cross-dependencies
Notes: For efficient transactions, we want to order epochs without flushing.

## Slide 12: OFENCE: Ordering Fence
ST A=1
Volatile Memory Order
ST A=1
Persistence Order
Time
ST B=2
ST B=2
Thread 1
Thread 1
OFENCE
Orders stores preceding OFENCE before later stores
Happens Before
Notes: We use a primitive also found in other recent proposals. The ordering FENCE orders stores without making them durable synchronously. We can implement this very efficiently.

## Slide 13
Stores
CPU
Shared LLC
CPU
DRAM Controller
PM Controller
Persistent
Private L1
Private L1
Volatile
Persist Buffer
Front End
Persist Buffer
Front End
Persist Buffer
Back End
Loads + Stores
Loads
Base System + Persist Buffers
Notes: To see how this works, let's zoom in on our persist buffers. We combine the persist buffers in our examples for simplicity.

## Slide 14: Ordering Epochs without Flushing
CPU 1
Local TS
L1 Cache
25
A = 1 25
Persist Buffer
B = 1 25
A = 2 26
A = 1
26
ST A = 1
ST B = 1
LD R1 = A
OFENCE
ST A = 2
B = 1
A = 2
Notes: A timestamp mechanism is utilized to order epochs. The local timestamp register contains the epoch timestamp of the currently inflight epoch, which is 25 in this example. CPU 1 is executing two epochs. Store A and B from the first epoch update the cache as well as the PB. The timestamp 25 is stored as part of each of their PB entries. The OFENCE simply marks the end of the epoch by incrementing the timestamp register to 26. The second epoch also has a store to A which clobbers the value in the caches, while creating a new PB entry.

## Slide 15: ACID Transactions in HOPS
Acquire Lock
Release Lock
Prepare Log Entry
1
N
Mutate Data Structure
1
N
Commit Transaction
Volatile Writes
Persistent Writes
OFENCE
NOT DURABLE!
Notes: So now we can have fast ACID transactions. SUPERB. WRONG. We forgot to guarantee durability. To solve this problem, we turn to sports. As fans of any sports team will tell you, good offence is nothing without a good defence. So, we introduce our second primitive to guarantee durability of outstanding PM writes.

## Slide 16: ACID Transactions in HOPS
Acquire Lock
Release Lock
Prepare Log Entry
1
N
Mutate Data Structure
1
N
Commit Transaction
Volatile Writes
Persistent Writes
OFENCE
DFENCE

## Slide 17: DFENCE: Durability Fence
Makes the stores preceding DFENCE durable
ST A=1
ST A=1
Persistence Order
Time
ST B=2
ST B=2
Thread 1
Thread 1
DFENCE
Happens Before
Volatile Memory Order
Notes: If there are two stores from a thread with an DFENCE between them, ST B can only be committed after ST A is made persistent.

## Slide 18: Durability is important too!
CPU 1
Local TS
L1 Cache
26
Persist Buffer
A = 2 26
A = 1
ST A = 1
ST B = 1
LD R1 = A
OFENCE
ST A = 2
N. DFENCE
B = 1
A = 2

## Slide 19: Hands-off Persistence System (HOPS)
Volatile memory hierarchy (almost) unchanged
Order epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method for handling cross-dependencies
Notes: We found that self-dependencies are quite common, and most PM proposals stall on encountering this.

## Slide 20: Preserving multiple copies of cachelines
CPU 1
Local TS
L1 Cache
26
Persist Buffer
B = 1 25
A = 2 26
A = 1
ST A = 1
ST B = 1
LD R1 = A
OFENCE
ST A = 2
B = 1
A = 2
A = 1 25
Notes: We have already seen HOPS deal with self-dependencies though. Looking back at our earlier example, you may not have realized that the two writes to address A are a self-dependency. The latest value of A is found in the caches to handle reuse. Both versions of A are present in the persist buffers.

## Slide 21: Hands-off Persistence System (HOPS)
Volatile memory hierarchy (almost) unchanged
Orders epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method for handling cross-dependencies
Notes: For handling cross-dependencies, we have a slow but correct method which piggybacks on coherence mechanisms. This is too complex for a talk in the last session, so we won’t go into detials. Feel free to ask me a question, or read our ASPLOS 17 paper for more details.

## Slide 22: Outline
Motivation
HOPS Design
Evaluation
PM
HEAD
C
A
B
Chart: Normalized Speedup
| ctree | hashmap | echo | nstore | vacation | average
CLWB+Fence | 1 | 1 | 1 | 1 | 1 | 1
HOPS | 1.17 | 1.33 | 1.06 | 1.3 | 1.21 | 1.2
No-Flush | 1.67 | 1.59 | 1.18 | 1.49 | 1.25 | 1.41
?

## Slide 23: System Configuration
Evaluated using gem5 full-system mode with the Ruby memory model
Parameter | Setting
CPU Cores | 4 cores, OOO, 2Ghz
L1 Caches | private, 64 KB, Split I/D
L2 Caches | private, 2 MB
DRAM | 4GB, 40 cycles read/write latency
PM | 4GB, 160 cycles read/write latency
Persist Buffers | 64 entries

## Slide 24: Performance Evaluation
Baseline + Persistent Write Queue
Ideal performance, unsafe on crash
Chart: Normalized Runtime
| echo | ycsb | redis | ctree | hashmap | vacation | average
x86-64 (NVM) | 1 | 1 | 1 | 1 | 1 | 1 | 1
x86-64 (PWQ) | 0.83333 | 0.83333 | 0.76923 | 0.86207 | 0.91045 | 0.93847 | 0.85422
HOPS (NVM) | 0.73333 | 0.56667 | 0.67692 | 0.7931 | 0.90832 | 0.90665 | 0.75795
HOPS (PWQ) | 0.73333 | 0.55574 | 0.67692 | 0.78578 | 0.83156 | 0.90877 | 0.74319
IDEAL (NON-CC) | 0.49167 | 0.41667 | 0.45385 | 0.75862 | 0.71015 | 0.77893 | 0.59369
(Lower is Better)
Baseline, uses clwb + sfence
HOPS
HOPS + Persistent Write Queue
Notes: RGB values =
102,194,165
252,141,98
141,160,203
231,138,195
166,216,84

## Slide 25: WHISPER Analysis HOPS Design
4% accesses to PM, 96% to DRAM
5-50 epochs/transaction
Self-dependencies common
Cross-dependencies rare
Volatile memory hierarchy (almost) unchanged
Order epochs without flushing
Allows multiple copies of same cacheline
Correct, conservative method based on coherence
Notes: Volatile memory (almost) unchanged
Allows multiple copies of same cacheline

## Slide 26: Questions?
Thanks!

## Slide 27: BENCHWARMERS

## Slide 28: Handling Cross Dependencies
Local TS
L1 Cache
25
Local TS
L1 Cache
14
Persist Buffer
ST A = 4
CPU 1
CPU 0
Directory
1
2
3
0:25
A = 1
A = 4 14
A = 4
0:25
24

## Slide 29: Comparison with DPO (Micro 16)
Parameter | HOPS | DPO
Primitives |  Ordering, Durability | × Ordering
Conflicts | Buffered |  Buffered
Effect on Volatile accesses | None | × Fully associative PBs snooped on every coherence request
Scalable to multiple cores | Lazy (cumulative) updates of PB drain | × Global Broadcast on every PB drain
Scalable to multiple MC |  Works natively | × Designed for one MC

## Slide 30: Comparison with Efficient PB (Micro 15)
Parameter | HOPS | Efficient PBs
Primitives |  Ordering, Durability | × Ordering
Intra-thread Conflict | Buffered | × Causes Synchronous Flush
Inter-thread Conflict | Buffered |  Buffered (upto 5)
Cache modifications |  1 bit | × Proportional to number of cores, inflight epochs supported

## Slide 31: Comparison with Non-Temporal Stores (x86)
Parameter | HOPS | NT Stores
Stores cached | Yes | × Cache copy invalidated
Ordering Guarantees | Yes, with fast OFENCE |  Yes, with slower FENCEs
Durability Guarantees | Yes, with DFENCE | × No

## Slide 32: Linked List Insertion - Naive
Create Node
Update Node Pointer
Update Head Pointer
CACHE
HEAD
NODE C
NODE A
NODE B
PM
HEAD
NODE C
NODE A
NODE B
CACHE WRITEBACK
Notes: This involves three separate updates- the node creation and the two pointers.
Head pointer is written back OOO. Inconsistent because Node C doesn’t point to Node A, and thus Nodes A and B are not reachable.

## Slide 33: Linked List Insertion - Naive
Caches (volatile) wiped clean
Main Memory inconsistent!
CACHE
HEAD
NODE C
NODE A
NODE B
PM
HEAD
NODE C
NODE A
NODE B
System Crash
?

## Slide 34: Linked List Insertion – Crash Consistent
Create Node
Update Node Pointer
FLUSH EPOCH 1
Update Head Pointer
FLUSH EPOCH 2
CACHE
HEAD
NODE C
NODE A
NODE B
PM
HEAD
NODE C
NODE A
NODE B
CACHE WRITEBACK
Epoch 1
Epoch 2
EXPLICIT WRITEBACK
Notes: We can fix this by grouping updates into ordered epochs, and flushing each epoch to PM before starting next one. This is consistent because the head always points to a valid linked list at each point

## Slide 35: Performance Evaluation
Chart: Normalized Runtime
| echo | ycsb | redis | ctree | hashmap | vacation | average
x86-64 (NVM) | 1 | 1 | 1 | 1 | 1 | 1 | 1
x86-64 (PWQ) | 0.83333 | 0.83333 | 0.76923 | 0.86207 | 0.91045 | 0.93847 | 0.85422
HOPS (NVM) | 0.73333 | 0.56667 | 0.67692 | 0.7931 | 0.90832 | 0.90665 | 0.75795
HOPS (PWQ) | 0.73333 | 0.55574 | 0.67692 | 0.78578 | 0.83156 | 0.90877 | 0.74319
IDEAL (NON-CC) | 0.49167 | 0.41667 | 0.45385 | 0.75862 | 0.71015 | 0.77893 | 0.59369
(Lower is Better)
Baseline, uses clwb + sfence
Baseline + Persistent Write Q
HOPS
HOPS + Persistent Write Q
Ideal performance, incorrect on crash
Notes: RGB values =
102,194,165
252,141,98
141,160,203
231,138,195
166,216,84

## Slide 36: Proposed Use-Cases
File Systems
  Existing FS (ext4)
  NVM-aware FS (PMFS, BPFS)
Persistent Data stores
  Key-Value stores
  Relational databases
Persistent Heap
Various forms of caching
  Webserver/file/page caching
Low-power data storage for IoT devices
Notes: Maybe do away with this slide?

## Slide 37: Intel extensions for PM
CLWB - Cache line Write Back
  Write back cached line (if present in cache hierarchy), may retain clean copy
Notes: When should I introduce epochs?

## Slide 38: Evaluating Intel extensions
Crash-Consistency
  Sufficient to provide crash consistency, if used correctly
Programmability
  Pushes burden of data movement onto programmer
Performance
  Provides ordering and durability mixed in one
Notes: SHOW ANIMATION ABOUT WHY THE EXTENSIONS MAKE CACHES FUNCTIONALLY VISIBLE?

## Slide 39: Evaluating Intel extensions
Crash-Consistency
  Sufficient to provide crash consistency, if used correctly
Programmability
  Pushes burden of data movement onto programmer
  Complex ordering guarantees, expressed in imprecise prose
  Complex semantics, expressed in imprecise prose
  Makes the programmer worry about caches
Notes: SHOW ANIMATION ABOUT WHY THE EXTENSIONS MAKE CACHES FUNCTIONALLY VISIBLE?

## Slide 40
Coherent Cache Hierarchy
B=0
B=1
CPU
Persistent Address Space
Program
1. A = 1
2. B = 1
3. CLWB A
4. CLWB B
Caches -> Memory Controller Queues
A=0
A=0
B=0
Persistent Write Queue
(PM Controller)
A=1
Notes: Need to replace this with a simpler figure that makes more sense.

## Slide 43: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
Persist Buffer
L1 Cache

## Slide 44: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
25
Persist Buffer

## Slide 45: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
25
A = 1
A = 1 25
Persist Buffer
ST A = 1

## Slide 46: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
25
A = 1
A = 1 25
Persist Buffer
ST A = 1
ST B = 1
B = 1
B = 1 25

## Slide 47: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
26
A = 1
A = 1 25
Persist Buffer
ST A = 1
ST B = 1
OFENCE
B = 1
B = 1 25

## Slide 48: Intra-thread Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
26
A = 2
A = 1 25
Persist Buffer
ST A = 1
ST B = 1
OFENCE
ST A = 2
B = 1
B = 1 25
A = 2 26

## Slide 49: Intra-thread Dependency (Epoch) : Enforce EXAMPLE TO BE DROPPED
Drain requests for all entries in epoch sent concurrently
Epoch entries drained after all drain ACKs received for previous epoch
A = 1 25
Persist Buffer
B = 1 25
A = 2 26
PM Controller
PM Region
PM Controller
PM Region
ST A = 1
ST B = 1

## Slide 50: Intra-thread Dependency (Epoch) : Enforce
Drain requests for all entries in epoch sent concurrently
Epoch entries drained after all drain ACKs received for previous epoch
A = 1 25
Persist Buffer
B = 1 25
A = 2 26
PM Controller
PM Region
PM Controller
PM Region
ACK
ACK
A = 1
B = 1

## Slide 51: Intra-thread Dependency (Epoch) : Enforce
Drain requests for all entries in epoch sent concurrently
Epoch entries drained after all drain ACKs received for previous epoch
Persist Buffer
A = 2 26
PM Controller
PM Region
PM Controller
PM Region
A = 1
B = 1
ST A = 2

## Slide 52: Inter-thread Dependency : EXAMPLE TO BE DROPPED
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:24 1:14
Persist Buffer 0
C = 2 24 -
Global TS
Notes: Talk of local copy optimization

## Slide 53: Inter-thread Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:24 1:14
Persist Buffer 0
C = 2 24 -
Global TS
Flush Stalled (24 < 25)
Notes: Talk of local copy optimization

## Slide 54: Inter-thread Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:24 1:14
Persist Buffer 0
C = 2 24 -
DFENCE
Global TS
C = 1
Notes: Talk of local copy optimization

## Slide 55: Inter-thread Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:24 1:14
Persist Buffer 0
C = 2 24 -
DFENCE
Global TS
ACK
Notes: Talk of local copy optimization

## Slide 56: Inter-thread Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:25 1:14
Persist Buffer 0
Global TS
Notes: Talk of local copy optimization

## Slide 57: Intra-thread Dependency (Epoch) : Track ANIMATION WIP
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering persist barrier
CPU 1
Local TS
L1 Cache
26
A = 1 25
Persist Buffer
ST B = 1
OFENCE
ST A = 2
B = 1 25
A = 2 26
ST A = 1
ST A = 1
ST A = 1

## Slide 58: Inter-thread Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this on DFENCEs
Persist Buffer 1
PM Controller
PM Region
A = 4 14 0:25
0:25 1:14
Persist Buffer 0
Global TS
Flush OK
Notes: Talk of local copy optimization

## Slide 59: Draining writes to multiple PM Controllers
PM Controller
PM Controller
Persist Buffer
PM Region
B = 2
OFENCE
PM Region
A = 1
A = 3
PM Controller

## Slide 60: Loose Ends
PM addresses identified based on higher order address bits
PBs flushed on context switches using durable persist barriers
LLC misses to PM stalled if address present in PB
  Tracked using counting bloom filters at the PM Controller
  Rare as updates stay longer in the cache than in PBs

## Slide 61: Reorder within an Epoch
ST A=1
Global Visibility
Persistence Order
Time
ST B=2
Epoch 1
Epoch 1
ST C=3
Epoch 2
OFENCE
ST A=1
ST B=2
ST C=3

## Slide 62: Inter-thread Dependency : Track ANIMATION PENDING
Identified using coherence activity
Loss of exclusive permissions signals inter-thread conflict
Local TS, Thread ID sent as part of coherence response (pessimistic)
Recorded in next epoch entry
Persist Buffer
Directory
Local TS
L1 Cache
25
A = 1
Local TS
L1 Cache
14
ST A = 4
CPU 1
CPU 0
1
Notes: Bloom filter to show all accesses since last durPB.

## Slide 63: Inter-thread Dependency : Track
Identified using coherence activity
Loss of exclusive permissions signals inter-thread conflict
Local TS, Thread ID sent as part of coherence response (pessimistic)
Recorded in next epoch entry
Local TS
L1 Cache
25
Local TS
L1 Cache
14
Persist Buffer
ST A = 4
CPU 1
CPU 0
Directory
1
2
A = 1

## Slide 64: Inter-thread Dependency : Track
Identified using coherence activity
Loss of exclusive permissions signals inter-thread conflict
Local TS, Thread ID sent as part of coherence response (pessimistic)
Recorded in next epoch entry
Local TS
L1 Cache
25
Local TS
L1 Cache
14
Persist Buffer
ST A = 4
CPU 1
CPU 0
Directory
1
2
3
A = 1
0:25

## Slide 65: Inter-thread Dependency : Track
Identified using coherence activity
Loss of exclusive permissions signals inter-thread conflict
Local TS, Thread ID sent as part of coherence response (pessimistic)
Recorded in next epoch entry
A = 4 14 0:25
Persist Buffer
Directory
Local TS
L1 Cache
25
Local TS
L1 Cache
14
ST A = 4
CPU 1
CPU 0
A = 4

## Slide 66: Cross Dependency : Enforce
Global TS register stored at LLC
Records <Thread ID:Flushed Epoch TS>
PBs check this before flushing epoch
PBs update this lazily
66
Notes: Talk of local copy optimization

## Slide 67: Key Idea 1
Support separate hardware primitives for ordering and durability

## Slide 68: Epoch Persistency [1]
Stores to different PM addresses within an epoch can be reordered among themselves, but not across epoch boundaries in the same thread
Stores to same PM address from any thread must be persisted as observed in global memory order
[1] Steven Pelley, Peter M. Chen, and Thomas F. Wenisch. 2014. Memory persistency, ISCA '14.
Notes: We implement the epoch persistency model

## Slide 69: Self Dependency (Epoch) : Enforce
Drain requests for all entries in oldest epoch sent concurrently
Next epoch drained after all drain ACKs received for previous epoch

## Slide 70: Self Dependency (Epoch) : Track
Local timestamp (TS) register maintained at L1 cache
Indicates epoch TS of current (incomplete) epoch
Local TS copied as part of PB entry for incoming PM stores
Local TS incremented on encountering OFENCE/DFENCE
CPU 1
Local TS
L1 Cache
25
A = 1 25
Persist Buffer
B = 1 25
A = 2 26
A = 1
26
ST A = 1
ST B = 1
OFENCE
ST A = 2
B = 1
A = 2

## Slide 71: Write Ordering in HOPS
Two types of dependencies preserved
  Cross dependencies between threads (address conflict)
  Self dependencies within a thread (epoch)
Dependencies identified at the time of insertion
Dependencies enforced at the time of drain into PM

## Slide 72: Draining writes to single PM Controller
A = 1
B = 1
A = 3
Persist Buffer
PM Region
A = 1 25
B = 1 25
A = 2 26
PM Controller
ACK (A)
ACK (B)