## Slide 1: Intelligent Power Management over Large Clusters
Stephen McGough*, Clive Gerrard*, Paul Haldane*, Sindre Hamlander+, Paul Robinson+, Dave Sharples*, Dan Swan*, Stuart Wheater+
* Newcastle University
+ Arjuna Technologies Ltd
Condor Week 2011

## Slide 2: Overview
What is the DI?
Background
Motivation
Power saving in Condor
Intelligent Power Management
Conclusion

## Slide 3: What is the DI?
Society is increasingly dependent on digital technologies
energy, transport, healthcare, commerce, engineering….
How can Newcastle researchers develop and harness these technologies to shape the future for everyone's benefit?
Research is increasingly dependent on digital technologies
record, store, analyse, model, share, visualise..
How can Newcastle researchers harness these technologies to do new, innovative research?
Institute Goals
Facilitate Internationally-Leading Research
  innovative, exciting, pioneering
  impact on researchers & society
Thriving, Inter-Disciplinary Research Community

## Slide 4: Background

## Slide 5: Condor at Newcastle
Using open access cluster computers around campus
  ~ 1300 Computers Windows Based
  ~ 250 Computers Linux Based
Using Staff Desktops
  ~ 3000 Computers (not all Condor enabled – yet!)
Using dedicated resources
  ~ 200 Computers in research groups around Campus
All computers at least dual core, moving to quad
  ~ 6000 – 10000 core cluster
Condor originally installed 5 years ago as ‘unsupported’ service. Now we’re making it a supported service

## Slide 6: Power Efficiency of Computers
Power Efficiency:
efficiency = flops/(PUE ∗ watts)
Flops/watts – pre-determined
  Average value used
Power Usage Effectiveness (PUE) – depends on location of computer (and time)
Type | flops | Wattage
Ultraslim Desktop | 941M | 54
CAD Computer | 1265M | 87
Legacy | 600M | 100

## Slide 7: Cluster Locations
Old Library
Basement Cluster room
Needs heating all year
PUE < 1 (offset heat from computers against room heating)
MSc Computing Cluster
South facing cluster room in High tower.
PUE > 1 (needs air-con all year)

## Slide 8: Motivation

## Slide 9: Motivation
University has strong desire to power down computers to save energy (money)
If a computer is not ‘working’ it should be powered down.
Windows XP Cluster
Windows 7 Cluster

## Slide 10: Motivation
Description | Number | %
Total number of jobs submitted to Condor | 642298 | 100%
- Which Completed | 469184 | 73%
- Without wasted time | 415807 | 65%
- With wasted time | 53377 | 8%
- Which were removed | 173114 | 27%
- Before execution | 164059 | 26%
- After some execution | 9055 | 1.4%
We have five years of condor logging to mine
  Other computers were used
    though this is the main log
  Initial analysis looks promising…

## Slide 11: Motivation
Total Time used by Condor | 51 years, 29 days, 20h, 2m, 52s | 100%
Total Wasted time | 33 years, 129 days, 4h, 6m, 13s | 65%
Total time wasted on jobs removed | 26 years, 33 days, 22h, 36m, 28s | 51%
Total time wasted on completed jobs | 7 years, 95 days, 5h, 29m, 45s | 14%
Total real job execution time | 17 years, 265 days, 15h, 56m, 39s | 35%
Further analysis didn’t look as good…
(Data from main Condor Submit computer – others exist)
For every 1 second of useful time we require ~3 seconds through Condor

## Slide 12: Average Wasted Time
(minutes)

## Slide 13: Rank
Rank used to express preference
Vast majority of people don’t use Rank
  Some who do get it wrong!
Rank Statement | % | Meaning
Null | 99.87% | No Preference
LoadAvg | 0.082% | Prefer computers with higher loads
((OpSys == "WINNT51")) + ((OpSys == "LINUX") * 2) | 0.047% | Prefer Linux to Windows
Memory | 0.0015% | Prefer computers with more memory
!!!
Notes: ((OpSys == "WINNT51")) + ((OpSys == "LINUX") * 2)
  300 times
  0.047% of jobs
0.00
  641459
  99.87% of jobs
LoadAvg
  529 times
  0.082% of jobs
Memory
  10 times
  0.0015% of jobs

## Slide 14: Aims
Reduce Power Consumption
Produce no impact on interactive machine users
Produce no impact on Condor users
Provide auditing on computing time used
On a cycle-scavenging Condor system.
All These Things can be done using Condor
  So What’s new?

## Slide 15: Power Saving in Condor

## Slide 16: What’s Wrong With Condor?
Nothing – Condor is “too good”, but…
  With a good administrator all this can be done
  With plenty of time this can be done
Put another way
  Administrators are busy people
  They have plenty of other tasks to do other than monitor and tweak Condor which gets along with things just fine
Most users don’t know enough Condor
  Can’t specify preferences over resources
  Only 3 users had done this at Newcastle – and one got it wrong

## Slide 17: Power Saving in Condor
Power rating (watts) and a PUE added to each worker description
Rank equation needs to be added to each job submission
Rank = flops/(PUE ∗ watts)
  Automatically added by our system
  And merged with user rank - if present

## Slide 18: Powering up and down
We use our own computer power-down script
  When no-one is using the computer
  When no Condor jobs are running
A persistent ClassAd is sent to Condor
  Indicates computer is powered down
Rooster can power up the computer
  If a job description requests this
  This calls our wakeup script

## Slide 19: Powering down Windows
We suspend computers
Windows can (wake up and) suspend for many reasons
  Not all under our control
    Anti-Virus updates, software updates
We can catch many of these
  But ~20% we can’t
We monitor the cluster for these
  Monitor condor_status for nodes which don’t update
  If a node fails to update ping it
    If it’s no longer there copy it’s last classad and post a fake replacement for a hibernating computer

## Slide 20: Intelligent Power Management

## Slide 21: Aims
Reduce Power Consumption
Produce no impact on interactive machine users
Produce no impact on Condor users
Provide auditing on computing time used
On a cycle-scavenging Condor system.
All These Things can be done using Condor
  So What’s new?
Do this all in a more automatic ‘intelligent’ way

## Slide 22
Arjuna's Agility is a federation tool
  Often used with Cloud Computing Platforms
Support structuring of the Cloud into federated sub-clouds through Service
Agreements
User configured (or implemented) policies can be installed to manage the interaction via Service Agreements

## Slide 23
Using Agility to provide intelligent management between parts of Condor
Adding in Rank
Deciding if a user has the right to power up computers
Monitoring activity and looking for anomalous behavior
Behavior is modified by the addition of new Agility policies
  A Service Agreement change will be accepted only if no Policy rejects it and at least one Policy accepts it
  Modification of Agility policies can lead to modification of the condor policies and/or modification of incoming jobs
Audit individuals' worker usage for potential billing

## Slide 24: General Architecture

## Slide 25: Job Submission Route

## Slide 26: Defined Policy
Favor Energy efficient computers
  Unless user states otherwise
Prioritize submissions
  Professors over PhD’s
Mark and manage Rogue jobs
  Jobs that have executed for too long
  Jobs that have been restarted too many times
  Jobs incorrectly submitted
Backlog reduction
  Modify above policy to deal with backlogs
Auditing
  Provide auditing for all jobs (per –user, -group, -school, -faculty, university)

## Slide 27: Auditing
Agility stores all attempted job runs. We can use this to provide audits of computer use
A job which takes n attempts to run consumes power of:
  Do we include evicted job time?
Can produce audit on user, group, school or university

## Slide 28: Future Policy
Federating between Condor Pools
Federating with the Cloud – Cloud Bursting
Resource profiling
  Working out when resources are idle and for how long
Job profiling
  Try to estimate job lengths for users
Dedicated workers for evictees
Running jobs on computers with active users
Education of users

## Slide 29: Conclusion
Condor is good
  Most users aren’t as good
  System administrators are busy
  They need tooling to automatically monitor and tweak the setup
This along with preferring power efficient computers and turning off computers can save a lot of energy (and money)

## Slide 30: Questions?
stephen.mcgough@ncl.ac.uk